## Slide 1
STRUCTURAL WIND ENGINEERING
Roland Wüchner, Chair of Structural Analysis, TUM
Máté Péntek, Chair of Structural Analysis, TUM
Structural Wind Engineering | Chair of Structural Analysis | WS 2018/19 | Detailed FSI
Chair of Structural Analysis
TUM Department of Civil, Geo and Environmental Engineering
Technical University of Munich

## Slide 2
  Presentation material from internal and external sources have been used either directly, modified or adapted to fit the purpose. Effort is continuously being made to accurately reference these. Nonetheless, check referencing in both the script as well as slides for completeness. In case of inconsistencies or mistakes please contact us!

## Slide 3: Content
From CFD to FSI
FSI – EIE:buffeting-induced vibration
FSI – IIE: vortex shedding-induced vibration
From FSI with SDoF towards MDoF
FSI of multiple interfering bodies
Towards a generic CWSI case

## Slide 4
  FROM CFD TO FSI

## Slide 5
  All steps will be shown going from a conceptual and theoretical view to the preparation of an example. For each step there will be a collection of files and tasks provided for individual study.

## Slide 6: The steps necessery for going from CFD to FSI
2D CFD example ⇒ representing a horizontal cut through a building
2D FSI example ⇒ representing model scenario for gust-induced buffeting
Inlet
Prescribed velocity
Structure
Non-moving
No slip condition
Outlet
Assigned pressure
Fluid
Navier-Stokes
Fractional-step solver
Wall
Slip-condition
CFD simulation results
CFD setup
Inlet
Prescribed velocity
Varying in time
Oscillating parabola
Structure
No slip condition
Moving
SDoF solver
FSI setup

## Slide 7: Custom inlet
From constant in time and space ⇒ varying in time and space: case of a pulsating inlet.
CFD setup
FSI setup
Custom inlet
Structural solver
Mesh mover
Coupling of physics and numerics
Power law
Constant parabolic
Constant

## Slide 8: Structural solver
The Generalized Alpha solver for SDoF ⇒ provided in the SDoF Python solver
CFD setup
FSI setup
Custom inlet ✓
Structural solver
Mesh mover
Coupling of physics and numerics
k
m
x
l0
cv
f(t) = f0 eiωt = a cos(ωt) + b sin(ωt)
t
x(t)
f ωn / 2k
0
2πωn
πωn
4πωn
6πωn
8πωn
10πωn

## Slide 9: Mesh mover
Example initial CFD mesh
Possible movement
Translation
Rotation
Bending
CFD setup
FSI setup
Custom inlet ✓
Structural solver ✓
Mesh mover
Coupling of physics and numerics

## Slide 10: Coupling of physics D-N
  Fluid solver ⇒ solves at timestep ⇒ pressure and friction on structure ⇒ forces on surface nodes ⇒ passed to structural solver as input
  Structural solver ⇒ SDoF solver for given forces reduced into center of gravity – Neumann condition for structure
CFD setup
FSI setup
Custom inlet ✓
Structural solver ✓
Mesh mover ✓
Coupling of physics and numerics
k
m
x
l0
cv

## Slide 11: Coupling of physics D-N
  Structural solver ⇒ SDoF solver results a displacement X
  Mesh solver ⇒ receives displacement as input from structural solver ⇒ solves ⇒ send the calculated mesh velocity to the fluid solver
  Fluid solver ⇒ takes the velocity input as Dirichlet condition ⇒ solves
  ⇒ The iteration loop goes on until a convergence criteria is met ⇒ refer back to the stong coupling for FSI problems
CFD setup
FSI setup
Custom inlet ✓
Structural solver ✓
Mesh mover ✓
Coupling of physics and numerics
k
m
x
l0
cv

## Slide 12
  FSI – EIE: BUFFETING-INDUCED VIBRATION

## Slide 13: FSI – buffeting tutorial
Based up on Tutorial 5 ⇒ StructWindEng_WS1718_GiDKratosTutorial_1_CFD2D
2D FSI example representing a horizontal cut through a building
Please make the modifications to the files in this example

## Slide 14: FSI – buffeting tutorial
Open with GiD the file you created on SWE_WS1819_GiDKratosTutorial_1_CFD2D
Apply an oscillating inlet velocity and ramp up time of 10 sec
Save as a new file
copy the contents of the folder “FSISDoFBuffeting” from “AuxiliaryFiles”
Rename “Projectparameters.json” to “ProjectParametersFSIBuffeting.json”
Copy “solver _settings” block from the “ProjectParametersFSIBuffeting_Template.json”
  ( check the next slide for picture)
open “ProjectParametersFSICSD.json” and check “model_part_name” matches the name given to your structural model part
Open “MainKratosFSIBuffeting.py” . In lines 138-150 check the group names in “ale_fixed-boundaries” are consistent with your example.
run “MainKratosFSIBuffeting.py”

## Slide 15: FSI – buffeting tutorial
ProjectParameters.json
ProjectParametersFSIBuffeting.json
ProjectParametersFSICSD.json

## Slide 16
  FSI – IIE: VORTEX SHEDDING-INDUCED VIBRATION

## Slide 17: FSI – vortex shedding-induced vibration tutorial
Based up on Tutorial 5 ⇒ SWE_WS1819_GiDKratosTutorial_1_CFD2D
2D FSI example representing a horizontal cut through a building
Please make the modifications to the files in this example

## Slide 18: FSI – vortex shedding-induced vibration tutorial
Open with GiD the file you created on SWE_WS1819_GiDKratosTutorial_1_CFD2D
Apply a constant inlet velocity and ramp up time of 10 sec
Save as a new file
copy the contents of the folder “FSISDoFVortexShedding” from “AuxillrayFiles”
Rename “Projectparameters.json” to “ProjectParametersFSIVortexShedding.json”
Copy “solver _settings” block from the “ProjectParametersFSIVortexShedding_Template.json”
  ( check the next slide for picture)
open “ProjectParametersFSICSD.json” and check “model_part_name” matches the name given to your structural model part
Open “MainKratosFSIVortexShedding.py” . In lines 138-150 check the group names in “ale_fixed-boundaries” are consistent with your example.
run “MainKratosFSIVortexShedding.py”

## Slide 19: FSI – buffeting tutorial
ProjectParameters.json
ProjectParametersFSIVortexShedding.json
ProjectParametersFSICSD.json

## Slide 20
  FROM FSI WITH SDOF TOWARDS MDOF

## Slide 21: Case of 3 x SDoF = MDoF
Nodal reactions from the CFD
Reaction magnitude
Concentrated action on the SDoF ⇒ here the MDoF can be seen and simplified into a superposition of SDoFs ⇒ a 3SDoF
A superposition of SDoFs ⇒ displacement_X + displacement_Y + rotation
(0,0)
Each SDoF
⇒ concentrated into a material point (to (0,0))
⇒ no shape + no dimension!

## Slide 22: FSI – 3SDoF tutorial
Based up on Tutorial 5 ⇒ SWE_WS1819_GiDKratosTutorial_1_CFD2D
Open with GiD the file you created on SWE_WS1819_GiDKratosTutorial_1_CFD2D
Apply a constant inlet velocity and ramp up time of 10 sec
Save as a new file
copy the contents of the folder “FSI3SDoF from “AuxillrayFiles”
Rename “Projectparameters.json” to “ProjectParametersFSI3SDoF.json”
Copy “solver _settings” block from the “ProjectParametersFSI3SDoF_Template.json”
open “ProjectParametersFSICSDSepRes.json” and “ProjectParametersFSICSDSepRes.json”, then check “model_part_name” matches the name given to your structural model part
Open “MainKratosFSIWithSepRes.py” . In lines 138-150 check the group names in “ale_fixed-boundaries” are consistent with your example.
run “MainKratosFSIWithSepRes.py”

## Slide 23: FSI – 3SDoF tutorial
ProjectParameters.json
ProjectParametersFSI3SDoF.json
ProjectParametersFSICSDVecRes.json

## Slide 24: Case of 3 x SDoF = MDoF
Reaction ⇒ result of the CFD simulation, here 2D case of horizontal cut ⇒ reaction extraction and „preparing/sending“ to the SDoF solver
Locate structure interface in fluid domain
Loop over the nodes on the interface
Extract reactions from the nodes
Reaction Y
Reaction X
Reaction magnitude

## Slide 25: Case of 3 x SDoF = MDoF
Node
Coordinates: node.X, node.Y, node.Z
Id number: node.Id
Nodal data: pressure, velocity, reaction, displacement
Retrieving nodal solutions – from the current time step using the commands:
  node.GetSolutionStepValue(PRESSURE, 0)
  node.GetSolutionStepValue(VELOCITY, 0)
  node.GetSolutionStepValue(REACTION, 0)
  node.GetSolutionStepValue(MESH_DISPLACEMENT, 0)
Interested in nodes on the interface of the structure ⇒ nodes part of a certain Sub Model Part
for node in main_model_part.GetSubModelPart(structure_submodel).Nodes
Reaction magnitude

## Slide 26: Case of 3 x SDoF = MDoF
Extract and apply appropriate action force for
⇒ displacement_X
⇒ displacement_Y
⇒ rotation
def ExtractForceX(nodes):
fx = 0.0
for node in nodes:
reaction = node.GetSolutionStepValue(REACTION, 0)
fx += -reaction[0]
return fx
def ExtractForceY(nodes):
fy = 0.0
for node in nodes:
reaction = node.GetSolutionStepValue(REACTION, 0)
fy += -reaction[1]
return fy
def ExtractMoment(nodes):
mz = 0.0
for node in nodes:
reaction = node.GetSolutionStepValue(REACTION, 0)
fx = -reaction[0]
fy = -reaction[1]
rx = node.X - 0.0
ry = node.Y - 0.0
mz += ry * fx - rx * fy
return mz
Some selected code snippets
Compare Exercise_08:
MainKratosFsiWithSepRes.py: lines 155-178
MainKratosFsiWithVecRes.py: lines 155-178

## Slide 27: Case of 3 x SDoF = MDoF
def RotateMirrorDisplace(theta, dispX, dispY, nodes):
for node in nodes:
rx0 = node.X0 - 0.0
ry0 = node.Y0 - 0.0
rx = cos(theta) * rx0 + sin(theta) * ry0
ry = -sin(theta) * rx0 + cos(theta) * ry0
dx = rx - rx0 + dispX
dy = ry - ry0 + dispY
node.SetSolutionStepValue(MESH_DISPLACEMENT_X, dx)
node.SetSolutionStepValue(MESH_DISPLACEMENT_Y, dy)
pitching_moment = ExtractMoment(Structure.Nodes)
reactionX = ExtractForceX(Structure.Nodes)
reactionY = ExtractForceY(Structure.Nodes)
structure_rotAlpha_solver.solveStructure(pitching_moment)
structure_dispX_solver.solveStructure(reactionX)
structure_dispY_solver.solveStructure(reactionY)
Calculate the DoFs using the respective structural solver for
⇒ displacement_X
⇒ displacement_Y
⇒ rotation
Solve for each structural solver separately
Compare :
MainKratosFsiWithSepRes.py: lines 307-314
MainKratosFsiWithVecRes.py: lines 335-341
Set displacement to the nodes on the surface of the structure ⇒ as a superposition of SDoFs
Compare Exercise_08:
MainKratosFsiWithSepRes.py: lines 165-174
MainKratosFsiWithVecRes.py: lines 165-174

## Slide 28: Case of 3 x SDoF = MDoF: important code snippets highlighted
# compute the residual for rotation
initial_residual1 = structure_rotAlpha_solver.getDisplacement() - pitching_angle old_residual1 = initial_residual1
residual1 = old_residual1
# compute the residual for displacement Y
initial_residual2 =structure_dispY_solver.getDisplacement() - displacementY old_residual2 = initial_residual2
residual2 = old_residual2
# compute the residual for displacement X
initial_residual3 = structure_dispX_solver.getDisplacement() - displacementX old_residual3 = initial_residual3
residual3 = old_residual3
while not ((abs(residual1) < abs_residual
or abs(residual1) < abs(initial_residual1) * rel_residual) and
(abs(residual2) < abs_residual
or abs(residual2) < abs(initial_residual2) * rel_residual) and
(abs(residual3) < abs_residual
or abs(residual3) < abs(initial_residual3) * rel_residual)):
old_residual1 = residual1
residual1 = structure_rotAlpha_solver.getDisplacement()- pitching_angle old_residual2 = residual2
residual2 = structure_dispY_solver.getDisplacement() - displacementY old_residual3 = residual3
residual3 = structure_dispX_solver.getDisplacement() – displacementX
Residuals computed and checked for each DoF separately
Compare : MainKratosFsiWithSepRes.py: lines 316-372
Compute the initial
residuals
Check for each residual separately if convergence is reached
Iterate between fluid and structure until convergence

## Slide 29: Case of 3 x SDoF = MDoF: important code snippets highlighted
def calcResidual(solution, old_solution):
residual = [0]*len(solution)
for index in range(len(solution)):
residual[index] = solution[index] - old_solution[index] return residual
# get Solution
rot = structure_rotAlpha_solver.getDisplacement()
dispX = structure_dispX_solver.getDisplacement()
dispY = structure_dispY_solver.getDisplacement()
Solution = [rot, dispX, dispY]
# compute the residual
residual = calcResidual(Solution, old_Solution)
residual_old = residual
initResidual = residual
while not ( L2Norm(residual) < abs_residual
or L2Norm(residual) < L2Norm(initResidual)*rel_residual):
# compute the residual
residual_old = residual
residual = calcResidual(Solution, old_Solution)
Residuals for each DoF combined in a vector ⇒ vector norm checked for convergence
Compare : MainKratosFsiWithVecRes.py: lines 201-205 and lines 343-396
Define function to compute residual
Create vector with results
Compute the initial residual and check if convergence is reached
Iterate between fluid and structure until convergence

## Slide 30
  FSI OF MULTIPLE INTERFERING BODIES
[B. Chandra, H. L. Weng, S.v. Wenczowski, M. Péntek, A. Winterstein: Partitioned Multi-Physics Simulation of Interfering Square Cylinders in a Flow, FEM for FSI project, Statik TUM, 2017]

## Slide 31: FSI: modeling of multiple interfering bodies
Open in GiD postprocess Version1 and Version2 results from “ FSIInterfering“

## Slide 32
  TOWARDS A GENERIC FSI CASE

## Slide 33: Differences compared to the example of the horizontal cut
  Structural solver ⇒ A generalized MDoF solver (X and Y displacement possible for each node of the structure ) ⇒ FEM formulation
  Coupling of physics and numerics
  ⇒ using matching grids: each node of the interface of the structure has a corresponding node (with the same coordinates) in the fluid domain
  ⇒ the forces of the fluid are not reduced to a certain point (previously center of gravity), but passed to the corresponding node in the structural solver
  ⇒ vectorial formulation of the residual for convergence
  ⇒ Fix-point and Aitken relaxation
CFD setup
FSI setup
Custom inlet ✓
Structural solver ✓
Mesh mover ✓
Coupling of physics and numerics ✓
Fluid
domain
Structure
domain

## Slide 34: FSI: Kratos CFD + Kratos CSD coupling – MDoF/general FEM case
Reaction ⇒ result of the CFD simulation, here 2D case of vertical cut ⇒ reaction extraction and „preparing/sending“ to the structural (generalized MDoF/FEM) solver
Locate structure interface in fluid domain
Loop over the nodes on the interface
Extract reactions from the nodes
Reaction Y
Reaction X

## Slide 35: Kratos CFD + Kratos CSD coupling – MDoF/general FEM case
Reaction magnitude
Node
Coordinates: node.X, node.Y, node.Z
Id number: node.Id
Nodal data: pressure, velocity, reaction, displacement
Retrieving nodal solutions – from the current time step using the commands:
  node.GetSolutionStepValue(PRESSURE, 0)
  node.GetSolutionStepValue(VELOCITY, 0)
  node.GetSolutionStepValue(REACTION, 0)
  node.GetSolutionStepValue(DISPLACEMENT, 0)
Interested in nodes on the interface of the structure ⇒ nodes part of a certain Submodel Part
for node in main_model_part_fluid.GetSubModelPart(structure) .Nodes:

## Slide 36: Kratos CFD + Kratos CSD coupling – MDoF/general FEM case
CFD – Reaction magnitude
⇒ needs to be „communicated/sent” to the structural solver
⇒ mesh size on the structure interface of the CFD domain is 3.0
5 x 3.0 = 15.0
5 x 3.0 = 15.0
5 x 3.0 = 15.0
5 x 3.0 = 15.0
2 x 7.5 = 15.0
2 x 7.5 = 15.0
CSD – Displacement magnitude
⇒ needs to be „communicated/sent” to the fluid (or mesh) solver
⇒ mesh size on the structure interface of the CSD domain is 3.0 (matching) and 7.5 (non-matching)

## Slide 37: Kratos CFD + Kratos CSD coupling ⇒ matching grid
CFD – Reaction magnitude
⇒ needs to be „communicated/sent” to the structural solver
⇒ mesh size on the structure interface of the CFD domain is 3.0
CSD – Displacement magnitude
⇒ needs to be „communicated/sent” to the fluid (or mesh) solver
⇒ mesh size on the structure interface of the CSD domain is 3.0 (matching the one on the CFD side)
Matching nodes on interface ⇒ needs a searching, matching and storing algorithm for pairing nodes

## Slide 38: Kratos CFD + Kratos CSD coupling ⇒ matching grid: important code snippets highlighted
for fluid_node in structure_interface.Nodes:
for struct_node in fluid_interface.Nodes:
if (abs(fluid_node.X - struct_node.X) < 1e-4) and (abs(fluid_node.Y - struct_node.Y) < 1e-4):
fluid_node.SetValue(PATCH_INDEX, struct_node.Id)
struct_node.SetValue(PATCH_INDEX, fluid_node.Id)
Find matching fluid and structure nodes ⇒ must have approx. the same coordinates
Compare Exercise_08: MainKratosFsiWithMatching.py: lines 242-250
Loop over all possible combinations of fluid and structure nodes at the interface
If the nodes of a combination have approx. the same coordinates ⇒ set them as a matching pair for FSI

## Slide 39: Kratos CFD + Kratos CSD coupling ⇒ matching grid: important code snippets highlighted
def NeumannToStructure(FluidNodes, StructNodes):
for fluid_node in FluidNodes:
StructNodes[fluid_node.GetValue(PATCH_INDEX)].SetSolutionStepValue(POINT_LOAD_X, 0,
-1*fluid_node.GetSolutionStepValue( REACTION_X, 0))
StructNodes[fluid_node.GetValue(PATCH_INDEX)].SetSolutionStepValue(POINT_LOAD_Y, 0,
-1*fluid_node.GetSolutionStepValue(
REACTION_Y, 0))
# Apply Neumann B.C.'s from fluid solver to structural solver
NeumannToStructure(structure_interface.Nodes, fluid_interface.Nodes)
Apply forces from fluid on structure
Compare Exercise_08: MainKratosFsiWithMatching.py: lines 264-271, 423, 460
Apply displacements of structure on fluid mesh
Compare Exercise_08: MainKratosFsiWithMatching.py: lines 273-276, 410, 449
def DisplacementToMesh(FluidNodes, StructNodes):
for struct_node in StructNodes:
FluidNodes[struct_node.GetValue(PATCH_INDEX)].SetSolutionStepValue(DISPLACEMENT_X,0,
struct_node.GetSolutionStepValue(DISPLACEMENT_X, 0))
FluidNodes[struct_node.GetValue(PATCH_INDEX)].SetSolutionStepValue(DISPLACEMENT_Y,0,
struct_node.GetSolutionStepValue(DISPLACEMENT_Y, 0))
# Apply Dirichlet B.C.'s from structural solver to mesh solver
DisplacementToMesh(structure_interface.Nodes, fluid_interface.Nodes)

## Slide 40: Kratos CFD + Kratos CSD coupling ⇒ non-matching grid
CFD – Reaction magnitude
⇒ needs to be „communicated/sent” to the structural solver
⇒ mesh size on the structure interface of the CFD domain is 3.0
CSD – Displacement magnitude
⇒ needs to be „communicated/sent” to the fluid (or mesh) solver
⇒ mesh size on the structure interface of the CSD domain is 3.0 (matching the one on the CFD side)
Matching nodes on interface ⇒ needs a searching, matching and storing algorithm for pairing nodes

## Slide 41: Kratos CFD + Kratos CSD coupling ⇒ non-matching grid
CFD – Reaction magnitude
⇒ needs to be „communicated/sent” to the structural solver
⇒ mesh size on the structure interface of the CFD domain is 3.0
CSD – Displacement magnitude
⇒ needs to be „communicated/sent” to the fluid (or mesh) solver
⇒ mesh size on the structure interface of the CSD domain is 7.5 (not matching the one on the CFD side)
Non-matching nodes on interface ⇒ each fluid node is connected to the closest 2 structural nodes ✓
Nodes on the interface – CFD domain
Nodes on the interface
– CSD domain
Assumption:
CFD mesh finer than
CSD on the interface

## Slide 42: Kratos CFD + Kratos CSD coupling ⇒ non-matching grid
Non-matching nodes on interface ⇒ each fluid node is connected to the closest 2 structural nodes ✓
F
Fa
Fb
F
Ra
Rb
b
a
L = a+b
Action/point load on the structure seen as a distance weighted value of the reaction of the fluid
Fb = F * wb = F * a / (a+b)
Fa = F * wa = F * b / (a+b)
⇒ analogy with the point load on a simply supported beam
⇒ structure nodes and respective weights (wa, wb) for each fluid node on the interface have to be searched for, computed and stored
⇒ one way of data transformation between different discretizations

## Slide 43: Kratos CFD + Kratos CSD coupling ⇒ non-matching grid
Non-matching nodes on interface ⇒ each fluid node is connected to the closest 2 structural nodes ✓
Displacement of the nodes on the structural interface of the CSD solver sent to the paired node on the fluid side
⇒ linear interpolation of the displacements Disp_Xb and Disp_Xa for the node of the fluid mesh
Disp_Xab = Disp_Xb * wb +
Disp_Xa * wa
⇒ using the respective weights (wa, wb) already calculated and stored
Action/point load on the structure seen as a distance weighted value of the reaction of the fluid
Fb = F * wb = F * a / (a+b)
Fa = F * wa = F * b / (a+b)
⇒ analogy with the point load on a simply supported beam
Disp_Xab
Disp_Xa
Disp_Xb
b
a
L = a+b
F
Fa
Fb
F
Ra
Rb
b
a
L = a+b

## Slide 44: Kratos CFD + Kratos CSD coupling ⇒ non-matching grid: important code snippets highlighted
def NeumannToStructureNonMatch(FluidNodes, StructNodes, fluid_CouplingMatrix):
for fluid_node in FluidNodes:
fluid_Coupling = fluid_CouplingMatrix[fluid_node.Id]
structNode_1_ID = fluid_Coupling[0]
structNode_2_ID = fluid_Coupling[1]
structNode_1_W = fluid_Coupling[2]
structNode_2_W = fluid_Coupling[3]
reactionX = -1* fluid_node.GetSolutionStepValue(REACTION_X, 0)
reactionY = -1* fluid_node.GetSolutionStepValue(REACTION_Y, 0)
reactionStructNode_1_X = reactionX*structNode_1_W
reactionStructNode_1_Y = reactionY*structNode_1_W
reactionStructNode_2_X = reactionX*structNode_2_W
reactionStructNode_2_Y = reactionY*structNode_2_W
reactionStructNode_1_X += StructNodes[structNode_1_ID].GetSolutionStepValue(POINT_LOAD_X,0)
reactionStructNode_1_Y += StructNodes[structNode_1_ID].GetSolutionStepValue(POINT_LOAD_Y,0)
reactionStructNode_2_X += StructNodes[structNode_2_ID].GetSolutionStepValue(POINT_LOAD_X,0)
reactionStructNode_2_Y += StructNodes[structNode_2_ID].GetSolutionStepValue(POINT_LOAD_Y,0)
StructNodes[structNode_1_ID].SetSolutionStepValue(POINT_LOAD_X, 0, reactionStructNode_1_X)
StructNodes[structNode_1_ID].SetSolutionStepValue(POINT_LOAD_Y, 0, reactionStructNode_1_Y)
StructNodes[structNode_2_ID].SetSolutionStepValue(POINT_LOAD_X, 0, reactionStructNode_2_X)
StructNodes[structNode_2_ID].SetSolutionStepValue(POINT_LOAD_Y, 0, reactionStructNode_2_Y)
Apply forces from fluid on structure
Compare Exercise_06: MainKratosFSI.py: lines 393-431
loop over all fluid nodes at interface
get corresponding two structure nodes and weights (stored in fluid_CouplingMatrix)
get the reaction force from the fluid node
compute the resulting reaction forces on the structure nodes
add the forces already subjected from other fluid nodes
set the summmed up forces on the nodes

## Slide 45: Kratos CFD + Kratos CSD coupling ⇒ non-matching grid: important code snippets highlighted
def DisplacementToMeshNonMatch(FluidNodes, StructNodes, fluid_CouplingMatrix):
for fluid_node in FluidNodes:
fluid_Coupling = fluid_CouplingMatrix[fluid_node.Id]
structNode_1_ID = fluid_Coupling[0]
structNode_2_ID = fluid_Coupling[1]
structNode_1_W = fluid_Coupling[2]
structNode_2_W = fluid_Coupling[3]
structNode_1_Disp_X = StructNodes[structNode_1_ID].GetSolutionStepValue(DISPLACEMENT_X, 0)
structNode_1_Disp_Y = StructNodes[structNode_1_ID].GetSolutionStepValue(DISPLACEMENT_Y, 0)
structNode_2_Disp_X = StructNodes[structNode_2_ID].GetSolutionStepValue(DISPLACEMENT_X, 0)
structNode_2_Disp_Y = StructNodes[structNode_2_ID].GetSolutionStepValue(DISPLACEMENT_Y, 0)
fluidNode_DispX = structNode_1_Disp_X*structNode_1_W + structNode_2_Disp_X*structNode_2_W
fluidNode_DispY = structNode_1_Disp_Y*structNode_1_W + structNode_2_Disp_Y*structNode_2_W
fluid_node.SetSolutionStepValue(DISPLACEMENT_X, 0, fluidNode_DispX)
fluid_node.SetSolutionStepValue(DISPLACEMENT_Y, 0, fluidNode_DispY)
Apply displacements of structure on fluid mesh
Compare Exercise_06: MainKratosFSI.py: lines 433-455
loop over all fluid nodes at interface
get corresponding two structure nodes and weights (stored in fluid_CouplingMatrix)
get the displacements of both structure nodes
compute the fluid node displacement by interpolation using the weights
set the displacement of the fluid node

## Slide 46: Kratos CFD + Kratos CSD coupling ⇒ non-matching grid map
Mapping algorithm for a matching grid
⇒ each fluid node is linked to the closest 2 structural nodes (for this case weigths 1 and 0)
Nodes in fluid mesh
Nodes in structure mesh
1
0
1
0
1
0
1
0
1
0
1

## Slide 47: Kratos CFD + Kratos CSD coupling ⇒ non-matching grid map
Mapping algorithm for a matching grid
⇒ each fluid node is linked to the closest 2 structural nodes (for this case weights 1.0 or 0.0)
Mapping algorithm for a non-matching grid
⇒ each fluid node is linked to the closest 2 structural nodes (for this case weights take values from the [0,1] interval)
Fluid Node ID StructNode1 ID StructNode2 ID StructNode1 weight StructNode2 weight
…
1421 18 20 0.984 0.016
1432 18 15 0.714 0.286
1438 15 18 0.587 0.413
1446 15 18 0.889 0.111
1452 15 13 0.81 0.19
1462 15 13 0.508 0.492
1468 13 15 0.794 0.206
1477 13 10 0.905 0.095
1484 13 10 0.603 0.397
1492 10 13 0.698 0.302
1501 10 13 1.0 0.0
Fluid Node ID StructNode1 ID StructNode2 ID StructNode1 weight StructNode2 weight
…
1421 146 138 1.0 0.0
1432 138 146 1.0 0.0
1438 129 122 1.0 0.0
1446 122 129 1.0 0.0
1452 114 107 1.0 0.0
1462 107 114 1.0 0.0
1468 101 97 1.0 0.0
1477 97 93 1.0 0.0
1484 93 97 1.0 0.0
1492 90 87 1.0 0.0
1501 87 90 1.0 0.0

## Slide 48: Kratos CFD + Kratos CSD coupling ⇒ non-matching grid: important code snippets highlighted
for fluid_node in structure_interface.Nodes:
f_X = fluid_node.X
f_Y = fluid_node.Y
ID_1 = 0
ID_2 = 0
dist_min = 1e12
dist_min2 = 1e12
for struct_node in fluid_interface.Nodes:
s_X = struct_node.X
s_Y = struct_node.Y
distance = sqrt(pow(f_X-s_X,2) + pow(f_Y-s_Y,2))
if distance < dist_min:
ID_2 = ID_1
dist_min2 = dist_min
ID_1 = struct_node.Id
dist_min = distance
elif distance < dist_min2 and distance > dist_min:
ID_2 = struct_node.Id
dist_min2 = distance
dist_A = dist_min
dist_B = dist_min2
dist_Abs = dist_A+dist_B
w_A = dist_B/dist_Abs
w_B = dist_A/dist_Abs
Find matching fluid and structure nodes
Compare Exercise_06: MainKratosFSI.py: lines 347-378
Loop over all fluid nodes
Determine the two structure nodes which are closest to the fluid node
Compute the weights of the structure nodes

## Slide 49: The goal ⇒ to you get familiar with the crucial components of CWSI
solve F
solve F
solve F
t
n
t
n-1
t
n+1
t
n+2
solve F
solve F
solve F
t
n
t
n-1
t
n+1
t
n+2
solve S
solve S
solve S
CFD
H
M
solve F
solve F
solve F
t
n
t
n-1
t
n+1
t
n+2
solve S
solve S
solve S
FSI = CFD + CSD
H
M
Pure CFD
One-Way Coupling
Two-Way Coupling
CFD
H
M
CSD
d
t
Achieved ✓

## Slide 50
  ADDITIONAL NOTES AND REMARKS

## Slide 51: When using a simplified (2D) setup of a skyscraper (3D)…
h = 600m
d
d
Vertical cut along
Horizontal cut along
V = 50 m/s
Real case / setup
Numerical wind-tunnel setup
assume h/d =10
square cross section
M
T
FD

## Slide 52: …be aware of the consequences of dimensional reduction
These are not the same !?!
2D setups…
Aiming to correspond to
the 3D setup
…actually corresponding to:
Vertical cut along
M
T
Horizontal cut along
FD
FL

## Slide 53: …be aware of the consequences due to modeling aspects („disclaimer“)
We are here running (mostly) 2D simulations of an inherently 3D physical phenomenon ⇒ recall that turbulence is a 3D phenomenon
Also large 3D phenomena in flow field are not captured, like e.g. „end effects“, „flow around sides“, …
Concerning turbulence: RANS model for 2D or running the LES(-type) simulations in 3D
Methodology, presented components and workflow are nonetheless valid
Presented tutorials are adequate for educational and prototyping purposes (limits the computational necessities: hardware, time, etc!)
Vertical cut along
M
T
Horizontal cut along
FD
FL

## Slide 54
  OUTLOOK

## Slide 55: Advanced topics: FSI in 3D & respective challenges ⇒ for e.g w.r.t. mapping…
How to map to a structure modeled and discretized by e.g. beam elements (dimensional reduction!)? → several application cases in wind engineering: bridges, towers, skyscrapers, wind turbine blades, …
CSD - beam
CFD – 2D
CFD – 3D
?!